## Slide 1
Enhancing Structural Test with Probabilistic Functional Information the first report
Advisor: Dworak, Jennifer(jdworak@smu.edu)
Zhang, Fanchen graduate Research Assistant (fzhang@smu.edu)
Thornton, Micah undergraduate Research Assistant (mathornton@smu.edu)

## Slide 2: Cell-aware fault Testing flow
Define
Cell-aware Fault
Insert
Scan Chain
Generate
Test Timing Template
(ATPG for Stuck-at)
Generate
Good-States
Cell-aware Fault Simulate
Tools
Output
Input
Mentor Graphic Tessent User Defined Fault Models(UDFM)
Cell-aware faults
Cell-aware faults file described by UDFM format
Mentor Graphic Tessent
Original circuit
Circuit with Scan Chain
Test procedure file
Mentor Graphic Tessent
Original circuit
Scan Chain test timing template
(it is the ATPG patterns for Stuck-at)
Synopsys Verilog Complier Simulator (VCS)
Synopsys Verilog Complier Simulator (VCS)
Good States
Mentor Graphic Tessent
Cell-Aware faults
Circuit with Scan Chain
Test Procedure file
Scan Chain test timing template
Good States
Fault simulation file
Fault Detected Dictionary
Notes: Explain the testing flow, it has 5 steps, the last two steps are most important. The third step(Generate Test Timing Template) is in order to obtaining Scan Chain test timing template ( describe how the scan chain work) and add it into our good-state patterns to make Tessent work, in following slides I explain it in detail.

## Slide 3: Define Cell-aware faults
Maps a set of defined faults to a specified library cell
Maps a set of defined faults to a specified instance
S386 Cell-aware fault defined in UDFM format
S386 circuit modified in UDFM format
Modified those cells by using library’s cell
Keep this cell without modified
Cell-aware faults are defined:
s386 UDFM file
s820 UDFM file
Notes: UDFM support three fault models defined. Here we use two: library cell and instance, Because we pay attention on Cell-aware fault, the Module model we did not employ. This slide shows how UDFM define and work on circuit’s Verilog file

## Slide 4: Insert Scan-chain
In this step, we obtained the circuit with scan chain and a test procedure file for testing.
Combinational Logic
Combinational Logic
Scan_in
Scan_out
D
Q
D
Q
D
Q
CLK
A circuit with a Scan Chain
DFFs with a Scan_Chain
S386 inserted a scan-chain
Test procedure
The test procedure file defines timing for scan chain load, shift and unload.
Circuits with Scan Chain:
s328_ScanChain
s820_ScanChain
Test procedure files:
s328_testproc
S820_testproc
Notes: This slide show how Scan-chain work on circuit’s Verilog and what does timing file for Scan-chain file look like. I think conventioneers are experts on testing area. Therefore I did not pay more attention on this slide and we don’t have to explain it in deeply.

## Slide 5: Generate Test Timing Template
In this step, by generating ATPG patterns for stuck-at faults,
we extracted testing header and tail for adding our Good-State testing file to make Tessent read and simulate
we also used ATPG patterns for stuck-at faults to test Cell-aware faults to compare our Good-State patterns effects
Header of s386 ATPG patterns file for S-at
In the header, it declares input, output clock pins and describes the timing procedure for Scan-Chain load, shift and unload. Also it generates a pattern to test the Scan-chain
Timing of testing procedure
Declare input, output and clock
Tail of s386 ATPG patterns file for S-at
In the tail, it describes the Scan-Chain
ATPG patterns for Stuck-at fault files:
S328_atpg_sat_patterns
S820_atpg_sat_patterns
Scan-Chain test
Notes: Here I explain the reason why we have “Generate Test Timing Template” step. It has two reasons as showed above. This way is a easy way to let Tesssent create timing file for scan-chain. If we want to define the timing file, I think we also can do it but it not good way to do in the current circumstances demand

## Slide 6: Generate the Good-State patterns: flow chart
Generate
Good-States
… …
… …
Creates random patterns
Simulate these patterns by VCS
Grab Good-State patterns
Tools
Input
Output
Perl script
None
Random input patterns
VCS
Test Bench of Verilog
Random input patterns
Good-State Patterns
s386 Random input patterns
All pins’ order are same with original circuit
s386 Good-State patterns
All pins’ order are same with Scan-Chain circuit. The input patterns include clock pin(the first one)
Input
Q
D
Output
The first three or more Good-State will be dropped because they are unstable
Random input patterns:
s328_PI
s820_PI
Test Bench:
s328_tb
s820_tb
Good-State patterns:
s328_goodstate
s820_goodstate
Notes: This slide show three detail steps in Generate Good-states. Actually the second and third step are worked together. The reason I separate it into two is I want to present it clearly. Here need to notice the pins’ order are different in input patterns and Good-state patterns, the reason is Good-state patterns is for simulating scan-chain circuit.

## Slide 7: Generate the Good-State patterns: timing of Good-Sate
Input:
1st Random pattern
Grab: Good-State1
1st input Random pattern, for state 1 PI
Q value, for state 1 Chain Load
D value, for state 1 Chain Unload
Output, for state 1 PO
0
2
20
18
40
38
22
Combinational Logic
Output
DFF
input
D
Q
Combinational Logic
Output
DFF
input
D
Q
Q
×××
Clock period = 20 time unit
Clock
Time Frame Expansion
… …
Output 1
Q 1
D 1
Input 1
Output 2
Q 2
D 2
Input 2
Good-State 1
Good-State 2
… …
… …
Grab: Good-State 2
2nd input Random pattern, for state 2 PI
Q value, for state 2 Chain Load
D value, for state 2 Chain Unload
Output, for state 2 PO
Input:
2nd Random pattern
Notes: Try to use time frame expansion to explain how did we grab the good states

## Slide 8: Cell-aware Fault Simulate
Cell-aware Fault Simulate
… …
Creates Cell-Aware simulating patterns into multiple files, each file has 20 patterns
Insert Cell-Aware fault and simulates
Concatenate faultsim_files into one fault_sim file
Generates detected dictionary
Tools
Input
Output
Perl script
Good-State Patterns
Header and tail of ATPG patterns file
Good-State simulating file
Tessent by using UDFM
UDFM file
Scan Chain circuit
Good-State simulating file
Fautsim_files
Faut list
Perl script
Fautsim_files
Fautsim_file
Perl script
Fautsim_files
Faut list
Good-State file
fault_det_dic
s386 fault_sim file
s386 fault_det_dic file
sim_patterns
each fault in fault list order
s386 fault list file
Note: Since UDFM does not support multiple detection, we have to separate patterns into multiple files to simulate multiple times, and concatenate faultsim_files into one file
Good-State simulation files:
s328_sim_pat
s820_sim_pat
fault_sim files:
s328_faultsim
s820_faultsim
fault_list files:
s328_fault_list
s820_fault_list
fault detected dictionary:
s328_det_dic
s820_det_dic
Notes: Here because I use Yiwen code to generate fault detected dictionary, it require all sim-patterns in one file not into multiple files, there is one more step between step3 and step4 that Creates Cell-Aware simulating patterns into one file. This is code caused one more step, I don’t want to show it up. I can combine it into step 4 in the future work.

## Slide 9: Evaluating: Comparison of Detected for Cell-aware of ATPG, Stuck-at of APTG and Good-State patterns
Note: All results of Good-State come from 100,000 number of patterns
s38584 Cell-aware fault detected(12 faults) |  |  |  |  |  |  |  |  |  |  |  | 
 | /AND4_8/ OUT | /NAND4_28/ OUT | /NOR4_5/ OUT | /AND3_0/ OUT | /AND3_1/ OUT | /AND3_2/ OUT | /NAND3_0/ OUT | /NAND3_1/ OUT | /NAND3_2/OUT | /NOR3_0/ OUT | /NOR3_1/ OUT | /NOR3_2 /OUT
ATPG cell-aware | Y | Y | Y | Y | Y | Y | Y | Y | Y | Y | Y | Y
ATPG S-at | Y | Y | Y | Y | Y | Y | Y | Y | Y | Y | Y | Y
Good-State | Y | N | Y | Y | Y | Y | Y | Y | Y | N | Y | N
s820 Cell-aware fault detected (12 faults) |  |  |  |  |  |  |  |  |  |  |  | 
 | /AND4_9/ OUT | /NAND4_29/OUT | /NOR4_4/ OUT | /AND3_10/ OUT | /AND3_11/ OUT | /AND3_12/ OUT | /NAND3_3/OUT | /NAND3_4/OUT | /NAND3_5/OUT | /NOR3_9/ OUT | /NOR3_10/ OUT | /NOR3_11/ OUT
ATPG cell-aware | Y | Y | N (RE) | Y | N (RE) | Y | Y | Y | Y | Y | Y | Y
ATPG S-at | Y | Y | N | N | N | Y | Y | Y | Y | Y | Y | Y
Good-State | Y | Y | N | N | N | N | N | N | N | N | Y | Y
s386 Cell-aware fault detected (8 faults) |  |  |  |  |  |  |  | 
 | /AND4_0/OUT | /AND3_34/OUT | /AND3_35/OUT | /AND3_36/OUT | /AND3_37/OUT | /AND3_38/OUT | /AND3_39/OUT | /AND3_40/OUT
ATPG cell-aware | Y | Y | Y | Y | Y | Y | Y | Y
ATPG S-at | N | Y | Y | N | N | Y | Y | Y
Good-State | N | Y | Y | N | Y | Y | Y | Y
Good-State patterns are effectively to detect those faults affect the circuit function. That means we will focus on these faults and attempt to process Good-State patterns to make them more effective.

## Slide 10: Evaluating: Comparison of number of detected for S-at patterns, 5k Good-State and 10k Good-State patterns
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0
5000 patterns | 0 | 175 | 1974 | 0 | 175 | 1974 | 220 | 2124
10000 patterns | 0 | 354 | 3890 | 0 | 358 | 3890 | 454 | 4216
s386 faults detected times G-S
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
5000 patterns | 22 | 2068 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 56 | 34
10000 patterns | 45 | 4151 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 102 | 110
s820 faults detected times G-S
No. | 1 | 2 | 3 | 4
Fault | /AND4_0/OUT | /AND3_34/OUT | /AND3_35/OUT | /AND3_36/OUT
5k patterns | 0 | 175 | 1974 | 0
10k patterns | 0 | 354 | 3890 | 0
No. | 5 | 6 | 7 | 8
Fault | /AND3_37/OUT | /AND3_38/OUT | /AND3_39/OUT | /AND3_40/OUT
5k patterns | 175 | 1974 | 220 | 2124
10k patterns | 358 | 3890 | 454 | 4216
No. | 1 | 2 | 3 | 4 | 5 | 6
Fault | /AND4_9/OUT | /NAND4_29/OUT | /NOR4_4/OUT | /AND3_10/OUT | /AND3_11/OUT | /AND3_12/OUT
5k patterns | 22 | 2068 | 0 | 0 | 0 | 0
10k patterns | 45 | 4151 | 0 | 0 | 0 | 0
No. | 7 | 8 | 9 | 10 | 11 | 12
Fault | /NAND3_3/OUT | /NAND3_4/OUT | /NAND3_5/OUT | /NOR3_9/OUT | /NOR3_10/OUT | /NOR3_11/OUT
5k patterns | 0 | 0 | 0 | 0 | 56 | 34
10k pattern | 0 | 0 | 0 | 0 | 102 | 110
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0
80 patterns | 0 | 2 | 8 | 0 | 2 | 8 | 2 | 9
s386 faults detected times S-at
No. | 1 | 2 | 3 | 4
Fault | /AND4_0/ OUT | /AND3_34/ OUT | /AND3_35/ OUT | /AND3_36/OUT
80 PATs | 0 | 2 | 8 | 0
No. | 5 | 6 | 7 | 8
Fault | /AND3_37/OUT | /AND3_38/OUT | /AND3_39/OUT | /AND3_40/OUT
80 PATs | 2 | 8 | 2 | 9
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
115 patterns | 1 | 40 | 0 | 0 | 0 | 1 | 4 | 3 | 5 | 1 | 1 | 2
s820 faults detected times S-at
No. | 1 | 2 | 3 | 4 | 5 | 6
Fault | /AND4_9/OUT | /NAND4_29/OUT | /NOR4_4/OUT | /AND3_10/OUT | /AND3_11/OUT | /AND3_12/OUT
115 PATs | 1 | 40 | 0 | 0 | 0 | 1
No. | 7 | 8 | 9 | 10 | 11 | 12
Fault | /NAND3_3/OUT | /NAND3_4/OUT | /NAND3_5/OUT | /NOR3_9/OUT | /NOR3_10/OUT | /NOR3_11/OUT
115 PATs | 4 | 3 | 5 | 1 | 1 | 2
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
205 patterns | 5 | 2 | 2 | 0 | 38 | 4 | 19 | 11 | 12 | 15 | 46 | 7
s38584 faults detected times S-at
No. | 1 | 2 | 3 | 4 | 5 | 6
Fault | /AND4_8/OUT | /NAND4_28/OUT | /NOR4_5/OUT | /AND3_0/OUT | /AND3_1/OUT | /AND3_2/OUT
205 PATs | 5 | 2 | 2 | 0 | 38 | 4
No. | 7 | 8 | 9 | 10 | 11 | 12
Fault | /NAND3_0/OUT | /NAND3_1/OUT | /NAND3_2/OUT | /NOR3_0/OUT | /NOR3_1/OUT | /NOR3_2/OUT
205 PATs | 19 | 11 | 12 | 15 | 46 | 7
No. | 1 | 2 | 3 | 4 | 5 | 6
Fault | /AND4_8/OUT | /NAND4_28/OUT | /NOR4_5/OUT | /AND3_0/OUT | /AND3_1/OUT | /AND3_2/OUT
5k patterns | 192 | 0 | 163 | 1 | 1038 | 28
10k patterns | 351 | 0 | 335 | 4 | 2129 | 40
No. | 7 | 8 | 9 | 10 | 11 | 12
Fault | /NAND3_0/OUT | /NAND3_1/OUT | /NAND3_2/OUT | /NOR3_0/OUT | /NOR3_1/OUT | /NOR3_2/OUT
5k patterns | 423 | 403 | 0 | 0 | 829 | 0
10k patterns | 862 | 780 | 4 | 0 | 1585 | 0
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0
5000 patterns | 192 | 0 | 163 | 1 | 1038 | 28 | 423 | 403 | 0 | 0 | 829 | 0
10000 patterns | 351 | 0 | 335 | 4 | 2129 | 40 | 862 | 780 | 4 | 0 | 1585 | 0
With the size of circuit increasing, the number of detected for faults are decreased. Some faults are hard to be detected which are our future focus. ATPG for S-at faults patterns are also can detect some faults, we may combine the ATPG patterns with Good-State patterns to make testing more effectively.
s38584 faults detected times G-S

## Slide 11: Evaluating: Increase faults and Good-state patterns for s38584 benchmark based on 1st fault set
s38584 Cell-aware fault detected (1010 faults) |  |  |  |  |  |  |  |  |  |  |  |  | 
GATE | AND |  |  | NAND |  |  | OR |  |  | NOR |  |  | SUM
 | AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4 | 
Total number of gates | 4930 | 287 | 299 | 1618 | 236 | 272 | 2464 | 63 | 94 | 1063 | 105 | 17 | 11448
Total number of gates with fault | 100 | 200 | 200 | 50 | 75 | 75 | 80 | 50 | 80 | 30 | 60 | 10 | 1010
1st Fault set | i00/o1 | i000/o1 | i0000/o1 | i00/o0 | i000/o0 | i0000/o0 | i11/o0 | i111/o0 | i1111/o0 | i11/o1 | i111/o1 | i1111/o1 | 
Chart: 
| AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4
5,000 | 0.87 | 0.635 | 0.38 | 0.3 | 0.6933 | 0.6133 | 0.1 | 0.22 | 0.0375 | 0.7333 | 0.55 | 0.6
10,000 | 0.88 | 0.645 | 0.375 | 0.38 | 0.72 | 0.6267 | 0.1 | 0.2 | 0.05 | 0.7667 | 0.55 | 0.6
20,000 | 0.87 | 0.67 | 0.395 | 0.4 | 0.72 | 0.64 | 0.1 | 0.22 | 0.05 | 0.7333 | 0.5833 | 0.6
40,000 | 0.88 | 0.675 | 0.39 | 0.4 | 0.7733 | 0.64 | 0.1 | 0.22 | 0.05 | 0.8 | 0.6167 | 0.6
Chart: 
| AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4
5,000 | 87 | 127 | 76 | 15 | 52 | 46 | 8 | 11 | 3 | 22 | 33 | 6
10,000 | 88 | 129 | 75 | 19 | 54 | 47 | 8 | 10 | 4 | 23 | 33 | 6
20,000 | 87 | 134 | 79 | 20 | 54 | 48 | 8 | 11 | 4 | 22 | 35 | 6
40,000 | 88 | 135 | 78 | 20 | 58 | 48 | 8 | 11 | 4 | 24 | 37 | 6
Number of faults detected for each kind of gate
Number of faults detected
Chart: 
| 5000.0 | 10000.0 | 20000.0 | 40000.0
1st Pattern Set | 486 | 496 | 508 | 517
2nd Pattern Set | 485 | 496 | 508 | 518
486
496
508
517
Faults coverage of detected
Chart: 
| 5,000 | 10,000 | 20,000 | 40,000
1st Pattern Set | 0.4812 | 0.4911 | 0.503 | 0.5119
2nd Pattern Set | 0.4802 | 0.4911 | 0.503 | 0.5129
48.12%
49.11%
50.30%
51.19%
485
496
508
518
48.02%
49.11%
50.30%
51.29%
Faults coverage for each kind of gate
Chart: 
| AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4
5,000 | 87 | 129 | 74 | 15 | 51 | 46 | 8 | 10 | 4 | 22 | 33 | 6
10,000 | 87 | 128 | 78 | 15 | 56 | 46 | 8 | 10 | 4 | 24 | 34 | 6
20,000 | 88 | 134 | 79 | 18 | 55 | 48 | 8 | 10 | 4 | 23 | 35 | 6
40,000 | 88 | 135 | 79 | 21 | 57 | 49 | 8 | 11 | 4 | 23 | 37 | 6
Chart: 
| AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4
5,000 | 0.87 | 0.645 | 0.37 | 0.3 | 0.68 | 0.61333 | 0.1 | 0.2 | 0.05 | 0.73333 | 0.55 | 0.6
10,000 | 0.87 | 0.64 | 0.39 | 0.3 | 0.74667 | 0.61333 | 0.1 | 0.2 | 0.05 | 0.8 | 0.56667 | 0.6
20,000 | 0.88 | 0.67 | 0.395 | 0.36 | 0.73333 | 0.64 | 0.1 | 0.2 | 0.05 | 0.76667 | 0.58333 | 0.6
40,000 | 0.88 | 0.675 | 0.395 | 0.42 | 0.76 | 0.65333 | 0.1 | 0.22 | 0.05 | 0.76667 | 0.61667 | 0.6
1st Pat. Set
2nd
Pat. Set

## Slide 12: Evaluating: Increase faults and Good-state patterns for s38584 benchmark based on 2nd faults set
s38584 Cell-aware fault detected (1010 faults) |  |  |  |  |  |  |  |  |  |  |  |  | 
GATE | AND |  |  | NAND |  |  | OR |  |  | NOR |  |  | SUM
 | AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4 | 
Total number of gates | 4930 | 287 | 299 | 1618 | 236 | 272 | 2464 | 63 | 94 | 1063 | 105 | 17 | 11448
Total number of gates with fault | 100 | 200 | 200 | 50 | 75 | 75 | 80 | 50 | 80 | 30 | 60 | 10 | 1010
2nd Fault set | i00/o1 | i100/o1 | i1001/o1 | i00/o0 | i100/o0 | i1001/o0 | i11/o0 | i110/o0 | i1100/o0 | i11/o1 | i110/o1 | i1100/o1 | 
Chart: 
| AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4
5,000 | 0.87 | 0.575 | 0.3 | 0.26 | 0.7067 | 0.5067 | 0.1 | 0.34 | 0.0625 | 0.7333 | 0.7 | 0.5
10,000 | 0.87 | 0.63 | 0.335 | 0.36 | 0.72 | 0.5733 | 0.1 | 0.32 | 0.0625 | 0.7667 | 0.75 | 0.5
20,000 | 0.88 | 0.665 | 0.345 | 0.42 | 0.7333 | 0.5733 | 0.1 | 0.38 | 0.0625 | 0.7333 | 0.75 | 0.5
40,000 | 0.88 | 0.64 | 0.355 | 0.38 | 0.7333 | 0.6133 | 0.1 | 0.36 | 0.0625 | 0.7667 | 0.75 | 0.5
Chart: 
| AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4
5,000 | 87 | 115 | 60 | 13 | 53 | 38 | 8 | 17 | 5 | 22 | 42 | 5
10,000 | 87 | 126 | 67 | 18 | 54 | 43 | 8 | 16 | 5 | 23 | 45 | 5
20,000 | 88 | 133 | 69 | 21 | 55 | 43 | 8 | 19 | 5 | 22 | 45 | 5
40,000 | 88 | 128 | 71 | 19 | 55 | 46 | 8 | 18 | 5 | 23 | 45 | 5
Number of faults detected for each kind of gate
Number of faults detected
Chart: 
| 5000.0 | 10000.0 | 20000.0 | 40000.0
1st Pattern Set | 465 | 497 | 513 | 511
2nd Pattern Set | 478 | 494 | 508 | 521
465
497
513
511
Faults coverage of detected
Chart: 
| 5,000 | 10,000 | 20,000 | 40,000
1st Pattern Set | 0.4604 | 0.49208 | 0.50792 | 0.50594
2nd Pattern Set | 0.47327 | 0.48911 | 0.50297 | 0.51584
46.04%
49.21%
50.79%
50.59%
478
494
508
521
47.33%
48.91%
50.30%
51.58%
Faults coverage for each kind of gate
Chart: 
| AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4
5,000 | 88 | 126 | 59 | 15 | 55 | 37 | 8 | 16 | 5 | 22 | 42 | 5
10,000 | 87 | 128 | 65 | 17 | 54 | 41 | 8 | 19 | 5 | 23 | 42 | 5
20,000 | 87 | 132 | 67 | 20 | 56 | 45 | 8 | 17 | 5 | 23 | 43 | 5
40,000 | 88 | 134 | 74 | 20 | 55 | 46 | 8 | 19 | 5 | 23 | 44 | 5
Chart: 
| AND2 | AND3 | AND4 | NAND2 | NAND3 | NAND4 | OR2 | OR3 | OR4 | NOR2 | NOR3 | NOR4
5,000 | 0.88 | 0.63 | 0.295 | 0.3 | 0.7333 | 0.4933 | 0.1 | 0.32 | 0.0625 | 0.7333 | 0.7 | 0.5
10,000 | 0.87 | 0.64 | 0.325 | 0.34 | 0.72 | 0.5467 | 0.1 | 0.38 | 0.0625 | 0.7667 | 0.7 | 0.5
20,000 | 0.87 | 0.66 | 0.335 | 0.4 | 0.7467 | 0.6 | 0.1 | 0.34 | 0.0625 | 0.7667 | 0.7167 | 0.5
40,000 | 0.88 | 0.67 | 0.37 | 0.4 | 0.7333 | 0.6133 | 0.1 | 0.38 | 0.0625 | 0.7667 | 0.7333 | 0.5
1st Pat. Set
2nd
Pat. Set

## Slide 13: Evaluating: Comparison of number of detected for S-at patterns and 40k Good-State patterns for s38584 benchmark
Number of faults detected
Chart: 
| 1st fautls set | 2nd fault Set
stuck_@n3 | 527 | 508
stuck_@n7 | 538 | 524
40,000 | 518 | 521
527
518
508
521
Faults coverage
Chart: 
| 1st fautls set | 2nd fault Set
stuck_@n3 | 0.52178 | 0.50297
stuck_@n7 | 0.53267 | 0.51881
40,000 | 0.51287 | 0.51584
52.18%
51.29%
50.30%
51.58%
S-at EMD_n=3 patterns V.S. 40k Good-State
S-at EMD_n=7 patterns V.S. 40k Good-State
538
524
53.27%
51.88%
Chart: 
| RE | TI | Green | Blue | Yellow
Sales | 413 | 4 | 23 | 43 | 527
1st fault set
Overall detected distribution for fault set |  |  |  |  | 
Color | Represent |  |  | Number of detected | 
 | S-at ATPG | Good-state patterns | Cell-aware APTG | 1st fault set | 2nd fault set
Green | N | N | Y | 23 | 26
Blue | N | Y | Y | 43 | 65
Yellow | Y | N/Y | Y | 527 | 508
Chart: 
| RE | TI | Green | Blue | Yellow
Sales | 411 | 4 | 26 | 65 | 508
2nd fault set
Chart: 
| RE | TI | Green | Blue | Yellow
Sales | 413 | 4 | 25 | 30 | 538
1st fault set
Chart: 
| RE | TI | Green | Blue | Yellow
Sales | 411 | 4 | 23 | 52 | 524
2nd fault set
RE: redundant 413
TI: tied 4
RE: redundant 407
TI: tied 4
RE: redundant 413
TI: tied 4
RE: redundant 407
TI: tied 4
Overall detected distribution for fault set |  |  |  |  | 
Color | Represent |  |  | Number of detected | 
 | S-at ATPG | Good-state patterns | Cell-aware APTG | 1st fault set | 2nd fault set
Green | N | N | Y | 25 | 23
Blue | N | Y | Y | 30 | 52
Yellow | Y | N/Y | Y | 538 | 524

## Slide 14: Evaluating: Comparison of number of detected for S-at patterns and 40k Good-State patterns for s38584 benchmark
Chart: 
| /AND2_12/OUT | /AND2_79/OUT | /AND2_87/OUT | /AND2_92/OUT | /AND3_0/OUT | /AND3_4/OUT | /AND3_15/OUT | /AND3_61/OUT | /AND3_63/OUT | /AND3_98/OUT | /AND3_100/OUT | /AND3_141/OUT | /AND3_160/OUT | /AND4_26/OUT | /AND4_42/OUT | /AND4_51/OUT | /AND4_67/OUT | /AND4_72/OUT | /AND4_86/OUT | /AND4_91/OUT | /AND4_105/OUT | /AND4_117/OUT | /AND4_121/OUT | /AND4_126/OUT | /AND4_131/OUT | /AND4_143/OUT | /AND4_161/OUT | /AND4_163/OUT | /AND4_183/OUT | /AND4_189/OUT | /AND4_196/OUT | /NAND2_25/OUT | /NAND4_44/OUT | /NOR3_0/OUT | /NOR3_11/OUT | /NOR3_17/OUT | /NOR3_51/OUT | /NOR4_2/OUT | /OR3_21/OUT | /OR3_28/OUT | /OR3_49/OUT | /OR4_16/OUT | /OR4_73/OUT
# detected | 88 | 109 | 523 | 211 | 34 | 6 | 35 | 560 | 27 | 11 | 9 | 52 | 7 | 814 | 1674 | 23 | 11 | 4710 | 182 | 11 | 13 | 53 | 100 | 182 | 11 | 182 | 2253 | 59 | 47 | 460 | 182 | 4 | 2 | 264 | 63 | 2 | 159 | 1859 | 4 | 216 | 366 | 61 | 16
43 faults detected by Good-Sate but not ATPG S-at EMD n = 3 based on 1st faults set
Chart: 
65 faults detected by Good-Sate but not ATPG S-at EMD n = 3 based on 2nd faults set
Chart: 
| /AND2_12/OUT | /AND2_79/OUT | /AND2_92/OUT | /AND3_0/OUT | /AND3_4/OUT | /AND3_15/OUT | /AND3_61/OUT | /AND3_63/OUT | /AND3_98/OUT | /AND3_100/OUT | /AND3_141/OUT | /AND3_160/OUT | /AND4_51/OUT | /AND4_67/OUT | /AND4_86/OUT | /AND4_91/OUT | /AND4_117/OUT | /AND4_126/OUT | /AND4_131/OUT | /AND4_143/OUT | /AND4_161/OUT | /AND4_163/OUT | /AND4_183/OUT | /AND4_196/OUT | /NOR3_17/OUT | /NOR3_51/OUT | /OR3_21/OUT | /OR3_28/OUT | /OR4_16/OUT | /OR4_73/OUT
# detected | 88 | 109 | 211 | 34 | 6 | 35 | 560 | 27 | 11 | 9 | 52 | 7 | 23 | 11 | 182 | 11 | 53 | 182 | 11 | 182 | 2253 | 59 | 47 | 182 | 2 | 159 | 4 | 216 | 61 | 16
30 faults detected by Good-Sate but not ATPG S-at EMD n = 7 based on 1st faults set
Chart: 
| /AND2_12/OUT | /AND2_79/OUT | /AND2_92/OUT | /AND3_2/OUT | /AND3_4/OUT | /AND3_15/OUT | /AND3_27/OUT | /AND3_61/OUT | /AND3_63/OUT | /AND3_84/OUT | /AND3_98/OUT | /AND3_110/OUT | /AND3_141/OUT | /AND4_6/OUT | /AND4_9/OUT | /AND4_35/OUT | /AND4_48/OUT | /AND4_66/OUT | /AND4_67/OUT | /AND4_77/OUT | /AND4_79/OUT | /AND4_86/OUT | /AND4_87/OUT | /AND4_88/OUT | /AND4_91/OUT | /AND4_105/OUT | /AND4_117/OUT | /AND4_126/OUT | /AND4_128/OUT | /AND4_131/OUT | /AND4_136/OUT | /AND4_143/OUT | /AND4_144/OUT | /AND4_151/OUT | /AND4_161/OUT | /AND4_163/OUT | /AND4_165/OUT | /AND4_183/OUT | /AND4_196/OUT | /NAND3_69/OUT | /NAND4_46/OUT | /NAND4_58/OUT | /NOR3_17/OUT | /NOR3_51/OUT | /OR3_20/OUT | /OR3_21/OUT | /OR3_35/OUT | /OR3_37/OUT | /OR3_43/OUT | /OR3_44/OUT | /OR3_45/OUT | /OR4_40/OUT
# detected | 72 | 80 | 195 | 19 | 9 | 33 | 51 | 67 | 42 | 15 | 18 | 27 | 72 | 15 | 7 | 16 | 3 | 14 | 1422 | 257 | 5 | 127 | 2 | 416 | 1 | 24 | 1 | 127 | 20 | 11 | 6 | 127 | 205 | 1 | 147 | 9 | 28 | 129 | 234 | 8 | 5 | 9 | 6 | 40 | 86 | 210 | 17 | 1 | 63 | 2 | 26 | 129
52 faults detected by Good-Sate but not ATPG S-at EMD n = 7 based on 2nd faults set

## Slide 15: Conclusions & Next step work
Cell-aware faults can be detected by UDFM model of Mentor Graphic
ATPG for S-at patterns detect Cell-aware fault
Good-state patterns detect Cell-aware fault
Good-State patterns detect Cell-aware fault
Can detect those faults affect the circuit function
Some faults are hard to be detected
Conclusions:
Next step work:
Attempt to do experiment on Large circuit
ATPG for S-at patterns on Large circuit
Good-state patterns on Large circuit
Process Good-State patterns to make them more effective
Identify mandatory conditions
Identify hard faults
Find a way to process Good-State
Notes: These are my thoughts for conclusion and next step work. Maybe you have better ideas you can tell me let me modify.

## Slide 16: Q&A
Thank You!!!